## Slide 1: Process capability
From Shewhart charts to Lean Six Sigma

## Slide 2: Walter Andrew Shewhart (1891-1967) was an American physicist, engineer and statistician, known as the father of statistical quality control
Control charts and rules/tests
Control charts, also known as Shewhart charts or process-behavior charts, are a statistical process control tool used to determine if a manufacturing or business process is in a state of control. Controls charts detect changes in processes.
Control chart rules (i.e., out-of-control conditions) for determining assignable cause variation
  Data contain both signal and noise. Therefore, one must separate the signal must separate from the noise within the data to be able to extract information.
  The points on a control chart are stratified using colors and symbols to uncover causes of variation the process.
  Variation based on either common causes (a.k.a. noise, chance causes, non-assignable causes, natural patterns, random effects, random errors) or special causes (a.k.a. signals, sporaidic causes, assignable causes, unnatural patterns, systematic effects, systematic errors).
Example quotes
“Both pure and applied science have gradually pushed further and further the requirements for accuracy and precision. However, applied science, particularly in the mass production of interchangeable parts, is even more exacting than pure science in certain matters of accuracy and precision.”
“Assignable causes of variation may be found and eliminated.”
http://www.azquotes.com/author/44595-Walter_A_Shewhart

## Slide 3: William Edwards Deming (1900-1993) was an American engineer, statistician, professor, author, lecturer, and management consultant, known as a father of “System of Profound Knowledge"
“In 1927, Deming was introduced to Walter A. Shewhart of the Bell Telephone Laboratories by C.H. Kunsman of the United States Department of Agriculture (USDA). Deming found great inspiration in the work of Shewhart, the originator of the concepts of statistical control of processes and the related technical tool of the control chart, as Deming began to move toward the application of statistical methods to industrial production and management. Shewhart's idea of common and special causes of variation led directly to Deming's theory of management. Deming saw that these ideas could be applied not only to manufacturing processes, but also to the processes by which enterprises are led and managed. This key insight made possible his enormous influence on the economics of the industrialized world after 1950.”
“The Knowledge of variation involves understanding that everything measured consists of both "normal" variation due to the flexibility of the system and of "special causes" that create defects. Quality involves recognizing the difference to eliminate "special causes" while controlling normal variation. Deming taught that making changes in response to "normal" variation would only make the system perform worse. Understanding variation includes the mathematical certainty that variation will normally occur within six standard deviations of the mean.”
https://en.wikipedia.org/wiki/W._Edwards_Deming

## Slide 4: Customers feel the variance (a change in a process or business practice that may alter its expected outcome) in each transaction, each delivered/shipped product or service
https://www.ge.com/sixsigma/SixSigma.pdf

## Slide 5
https://www.youtube.com/watch?v=obSupUdTjV8

## Slide 6
https://www.linkedin.com/learning/six-sigma-green-belt/project-identification

## Slide 7: Six Sigma DMAIC (Define, Measure, Analyze, Improve and Control) is a closed-loop process for continued improvement which eliminate unproductive steps - systematic, scientific and fact based
http://dl4a.org/uploads/pdf/581SPC.pdf

## Slide 8
https://www.youtube.com/watch?v=obSupUdTjV8

## Slide 9: A set of graphical tools for planning and controlling quality
Control chart (also known as the Shewhart chart or process behaviour chart)
Histogram
Scatter diagram/plot
Pareto chart
Check sheet
Cause-and-effect diagram (also known as the "fishbone" or Ishikawa diagram)
Stratification (alternately, flow chart or run chart)
https://en.wikipedia.org/wiki/Seven_Basic_Tools_of_Quality

## Slide 10
http://dl4a.org/uploads/pdf/581SPC.pdf

## Slide 11: Control charts have had a long history of use in U.S. industries and in many offshore industries as well
Control charts are a proven technique for improving productivity
  The primary productivity killers in any operation are scrap and rework. “If you reduce scrap and rework, then productivity increases, cost decreases, and production capacity (measured in the number of good parts per hour) increases”.
Control charts provide diagnostic information
  The pattern of points on the control chart will contain information of diagnostic value that allows the implementation of a change in the process that improves its performance.
Control charts provide information about process capability
  An estimate of process capability based on the value of important process parameters and their stability over time.
Control charts prevent unnecessary process adjustment
  “A control chart can distinguish between background noise and abnormal variation; no other device including a human operator is as effective in making”.
Control charts are effective in defect prevention
  The control chart helps keep the process in control, which is consistent with the “do it right the first time” philosophy.
  If you do not have effective process control, you are paying someone to make a nonconforming product this distinction.
http://dl4a.org/uploads/pdf/581SPC.pdf

## Slide 12: Actions taken to improve a process
https://www.youtube.com/watch?v=OjJZMMBvI90
http://dl4a.org/uploads/pdf/581SPC.pdf

## Slide 13
“During the 1920s, W.A. Shewhart first proposed the use of control charts, which commonly bear his name as Shewhart control charts (Shewhart, 1931). The objective of Statistical Process Control (SPC) charts is to detect out-of-control signals indicating the existence of special causes that affect the process stability by providing a visual indication of the behavior of critical quality variables. In fact, Shewhart chart scheme tests the hypothesis that the process is still in control. This is certainly not enough for practical applications where the causes of the problem should be found and the production should be restored to its satisfactory operational state. It is the search for the out-of-control causes and reinstatement of the process that complete the SPC loop. The effectiveness of the use of control charts depends on the ability to recognize patterns. According to Western Electric Company (1958), there are 15 common types of Control Chart Patterns (CCPs). Among these 15 CCPs are eight basic CCPs, namely, (a) normal, (b) increasing trend, (c) decreasing trend, (d) cyclic, (e) systematic, (f) mixture, (g) upward shift, and (h) downward shift patterns, as shown in Fig. 1. All other CCPs are either special forms of these basic CCPs or a mixture of two or more basic CCPs. Only the normal pattern is consistent with the hypothesis that the process continues to operate without
assignable causes, and all other patterns are not and should be considered as unnatural.”

## Slide 14: A process that is operating in the presence of assignable/special causes is said to be an out-of-control process
Special cause variation is identified by points that follows the out-of-control conditions:
1 point is outside the control limits (the upper control limit = UCL and lower control limit = LCL)
8/9 points on the same size of the center line (CL)
6 consecutive points are steadily increasing or decreasing
14 consecutive points are alternating up and down
2 out of 3 consecutive points are more than 2 sigmas from the center line in the same direction
4 out of 5 consecutive points are more than 1 sigma from the center line in the same direction
15 consecutive points are within 1 sigma of the center line
8 consecutive points on either side of the center line with not within 1 sigma (i.e., more than 1 sigma from the center line)
http://dl4a.org/uploads/pdf/581SPC.pdf
https://analyse-it.com/docs/user-guide/processcontrol/shewhartcontrolchartrules

## Slide 15: Some Sensitizing Rules for Shewhart Control Charts
The Western Electric Handbook (1956) suggests a set of decision rules (1-4) for detecting nonrandom patterns on control charts. The zone based rules are as follows:
One or more points outside of the control limits
Two of three consecutive points outside the two-sigma warning limits but still inside the control limits
Four of five consecutive points beyond the one-sigma limits
A run of eight consecutive points on one side of the center line
Six points in a row steadily increasing or decreasing
Fifteen points in a row in zone C (both above and below the center line)
Fourteen points in a row alternating up and down.
Eight points in a row on both sides of the center line with none in zone C
An unusual or nonrandom pattern in the data
One or more points near a warning or control limit
http://dl4a.org/uploads/pdf/581SPC.pdf

## Slide 16
One or more points outside of the control limits
8/9 points on the same size of the center line (CL)
6 consecutive points are steadily increasing or decreasing
Eight popular pattern tests http://ac.aua.am/trietsch/web/CHAPTER%207.pdf
13/14 consecutive points are alternating up and down

## Slide 17
2 out of 3 consecutive points are more than 2 sigmas from the center line in the same direction
4 out of 5 consecutive points are more than 1 sigma from the center line in the same direction
15 consecutive points are within 1 sigma of the center line
Eight popular pattern tests http://ac.aua.am/trietsch/web/CHAPTER%207.pdf
8 consecutive points on either side of the center line with not within 1 sigma

## Slide 18: Phase I and Phase II of Control Chart Application
In phase I, a set of process data is gathered and analyzed all at once in a retrospective analysis, constructing trial control limits to determine if the process has been in control over the period of time where the data were collected, and to see if reliable control limits can be established to monitor future production.
In phase II, we use the control chart to monitor
the process by comparing the sample statistic for each successive sample as it is drawn
from the process to the control limits
http://dl4a.org/uploads/pdf/581SPC.pdf
https://analyse-it.com/docs/user-guide/processcontrol/shewhartcontrolchartrules

## Slide 19
https://www.youtube.com/watch?v=obSupUdTjV8

## Slide 20
https://www.linkedin.com/learning/six-sigma-green-belt/spc-charts-for-variables

## Slide 21
https://www.linkedin.com/learning/six-sigma-green-belt/spc-charts-for-attributes

## Slide 22
https://www.linkedin.com/learning/six-sigma-green-belt/spc-charts-for-variables

## Slide 23
http://dl4a.org/uploads/pdf/581SPC.pdf
exponentially weighted moving average (EWMA) control chart or cumulative sum (CUSUM) control chart and statespace models or autoregressive integrated moving average (ARIMA) models

## Slide 24
Let’s practise!

## Slide 25
UCL = 1,5+3*0,15 = 1,959 and LCL = 1,5-3*0,15 = 1,051
CL = mean, UCL = 1,7013 and LCL = 1,2987
Chart: I chart
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
X-bar | 1.5119 | 1.4951 | 1.4817 | 1.4712 | 1.4882 | 1.4492 | 1.5805 | 1.5343 | 1.5076 | 1.5134 | 1.5242 | 1.5284 | 1.3947 | 1.5261 | 1.4083 | 1.5344 | 1.4874 | 1.4573 | 1.5777 | 1.506 | 1.4691 | 1.539 | 1.5592 | 1.5688 | 1.5264
UCL | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95 | 1.95
LCL | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05 | 1.05
Wafer_1 | 1.3235 | 1.4314 | 1.4284 | 1.5028 | 1.5604 | 1.5955 | 1.6274 | 1.419 | 1.3884 | 1.4039 | 1.4158 | 1.5821 | 1.2856 | 1.4951 | 1.3589 | 1.5747 | 1.368 | 1.4163 | 1.5796 | 1.7106 | 1.4371 | 1.4738 | 1.5917 | 1.6399 | 1.5797
Wafer_2 | 1.4128 | 1.3592 | 1.4871 | 1.6352 | 1.2735 | 1.5451 | 1.5064 | 1.4303 | 1.7277 | 1.6697 | 1.7667 | 1.3355 | 1.4106 | 1.4036 | 1.2863 | 1.5301 | 1.7269 | 1.3864 | 1.4185 | 1.4412 | 1.5051 | 1.5936 | 1.4333 | 1.5243 | 1.3663
Wafer_3 | 1.6744 | 1.6075 | 1.4932 | 1.3841 | 1.5265 | 1.3574 | 1.8366 | 1.6637 | 1.5355 | 1.5089 | 1.4278 | 1.5777 | 1.4447 | 1.5893 | 1.5996 | 1.5171 | 1.3957 | 1.3057 | 1.6541 | 1.2361 | 1.3485 | 1.6583 | 1.5551 | 1.5705 | 1.624
Wafer_4 | 1.4573 | 1.4666 | 1.4324 | 1.2831 | 1.4363 | 1.3281 | 1.4177 | 1.6067 | 1.5176 | 1.4627 | 1.5928 | 1.3908 | 1.6398 | 1.6458 | 1.2497 | 1.1839 | 1.5014 | 1.621 | 1.5116 | 1.382 | 1.567 | 1.4973 | 1.5295 | 1.5563 | 1.3732
Wafer_5 | 1.6914 | 1.6109 | 1.5674 | 1.5507 | 1.6441 | 1.4198 | 1.5144 | 1.5519 | 1.3688 | 1.522 | 1.4181 | 1.7559 | 1.1928 | 1.4969 | 1.5471 | 1.8662 | 1.4449 | 1.5573 | 1.7247 | 1.7601 | 1.488 | 1.472 | 1.6866 | 1.553 | 1.6887
s

## Slide 26
CL= X-bar-bar, UCL = 1,693 and LCL = 1,318
CL = R-bar, UCL = 0,687 and LCL = 0
Evaluate the stability of the Range (R) chart before drawing any conclusions about the Averages (X-bar) chart - if the R chart is out of control, the control limits on the X-bar chart will be unreliable.
If the subgroup size > 8/9, the range chart is replaced by a chart of the subgroup standard deviation, or S chart.

## Slide 27
CL= X-bar-bar, UCL = 1,969 and LCL = 1,042
CL = s-bar, UCL = 0,294 and LCL = 0
X-s charts can be used for any subgroup size greater than 1. X-s charts should be used when the subgroup size is unequal, 10 or more. The standard deviation gives a better estimate of the variation in large subgroups than the range does.

## Slide 28
http://dl4a.org/uploads/pdf/581SPC.pdf

## Slide 29
Process capability - capability analysis measures the ability of a process to meet specifications when the process is in statistical control
X-bar = 1,5, StDev = 0,0671, n = 5, R-bar = 0,325 =>
Cp = [(1,5+3*0,0671) - (1,5-3*0,0671)] / 6*(0,325/2,059) = 0,425
The largest allowable value for a quality characteristic is called the upper specification limit (USL), and the smallest allowable value for a quality characteristic is called the lower specification limit (LSL). Specification limits on the process are established at ± three-sigma (i.e., standard deviation).
Process capability index (Cpk) = Minimum{(USL-X-bar)/3*StDev, (X-bar-LSL)/ 3*StDev}
IF Cpk ≥ 1 and Cpk ≤ Cp THEN the process is capable

## Slide 30
http://www.six-sigma-material.com/Data-Classification.html

## Slide 31
For example the number of invoices when the mean processing time is estimated, the standard deviation (s) is 20 minutes, the desired precision (d) is ± five minutes and we want to be 95% confident
For example the number of invoices when proportion of defects or percent defect rate is estimated, the desired precision (d) is ± 1 %, the proportion of interest (e.g., an error rate) is 5 % and we want to be 95% confident
https://www.linkedin.com/learning/six-sigma-black-belt/sample-sizes

## Slide 32
https://www.linkedin.com/learning/six-sigma-green-belt/descriptive-statistics
These include range, variance and standard deviation.
A distance or deviation of each data point from the mean
A standard deviation
Where the data is centered and how much variation there is?
dispersion